# GRADES AVAILABLE – HYUNDAI SERVO PREMIUM ENGINE OIL

# CHARACTERISTICS

| SAE GRADE | 15W-40 |
| --- | --- |
| Kin. Viscosity @ 100ºC, cSt | 13.5 – 15.5 |
| Flash Point, COC, ºC, Min | 135 |
| Pour Point, ºC, Max | (-) 24 |
| TBN, mg KOH/gm | 10 – 11.5 |

# Text boxes

# APPLICATION

Hyundai Servo Premium Engine Oil is recommended for Hyundai top-end petrol vehicles. It is also suitable for new generation.  It is tailored to the lubrication requirement of Engines complying to Euro III.

DESCRIPTION

Hyundai Servo Premium Engine Oil is high performance gasoline engine oil for top-end Hyundai vehicles.   These oils are blended from high viscosity index base stocks and contain proven additive system to meet the stated performance standards

# PERFORMANCE BENEFITS

- Superior performance in terms of oxidation stability, piston deposit control.

- Extra wear protection at high temperatures and severe operating conditions.

- Superior valve train wear control.

- Outstanding overall engine cleanliness and also provide long engine life.

- Excellent rust and corrosion protection.

- Catalytic Convertor Compatible.

# PERFORMANCE STANDARDS

- API SJ.

- ACEA A3/B3 – 2004.

# APPROVAL

- M/s. Hyundai Motors India Ltd for  Hyundai vehicles.