# GRADE AVAILABLE –LANCER ENGINE OIL

# CHARACTERISTICS

| SAE GRADE | 10W-30 |
| --- | --- |
| Kin. Viscosity @ 100ºC, cSt | 9.5 - 11 |
| Viscosity Index | 130 Min |
| Flash Point, COC, ºC, Min | 200 |
| Pour Point, ºC, Max | (-) 30 |
| TBN, mg KOH/gm | 9 - 11 |

# Text boxes

# APPLICATION

Lancer Engine Oil is recommended for lubrication of Lancer cars.

DESCRIPTION

Lancer Engine Oil is high performance engine oil for new generation Lancer vehicles.   These oils are blended from high viscosity index base stocks and contain additives to meet the stated performance standards.

# PERFORMANCE BENEFITS

- Superior performance in terms of oxidation stability, dispersancy characteristics and energy efficiency.

- Excellent sludge control and extra wear protection at high temperatures and severe operating conditions.

- Outstanding overall engine cleanliness and also provide long engine life.

- Fuel savings and low oil top up.

- Catalytic Convertor Compatible.

# PERFORMANCE STANDARDS

- Meets API SJ / CF 2.

# MANUFACTURERS APPROVAL

- Approved as genuine oil by M/s. Hindustan Motors Ltd for Lancer cars.