# GRADES AVAILABLE - SERVO GEAR AXLE 85W-140

# CHARACTERISTICS

| SAE GRADE | 85W-140 |
| --- | --- |
| Kinematic Viscosity cSt @ 100(C | 25 – 27 |
| Viscosity Index, Min. | 90 |
| Flash point (COC), (C Min. | 180 |
| Pour Point, (C Max. | (-) 18 |

# Text boxes

# PERFORMANCE STANDARDS

Servo Gear Axle 85W-140 meets

- API Service GL 5

- API MT 1

- MIL- PRF – 2105E

# PERFORMANCE BENEFITS

- Satisfy the lubrication requirements of different axles.

- Provide protection against wear, due to good EP characteristics

- Give long service life even under high temperature operation since it has excellent oxidation stability.

- Provide good protection against corrosion.

- Has potential for extended drain period compared to conventional API GL 5 oils.

DESCRIPTION

Servo Gear Axle 85W-140 oil is a heavy duty multigraded special purpose gear lubricant. This oil is blended from selected base stocks and contain specific additive package to provide extreme pressure, anti-rust-corrosion characteristics.

# APPLICATION

Servo Gear Axle 85W-140 oil is  recommended differentials / axles of heavy commercial vehicles.