GRADES AVAILABLE – SERVO LML  2T OIL

# CHARACTERISTICS

|  | Servo LML 2T Oil |
| --- | --- |
| Kinematic Viscosity @ 40(C, cSt | 48-70 |
| Flash Point (COC), (C, Min | 70 |
| Sulphated Ash, % Wt., Max | 0.25 |

# Text boxes

# PERFORMANCE BENEFITS

- Low exhaust smoke

- Maintains engine cleanliness

- Minimises spark plug fouling

- Reduces port deposits and ring sticking

- Prevents seizure and scuffing

- Is easily pumpable by oil injection system

- Ensures reduced oil consumption

# PERFORMANCE STANDARDS

Meets

- Latest JASO FC specifications.

# MANUFACTURERS APPROVAL

- M/s. LML Ltd. Kanpur has approved LML Servo 2T Oil for two stroke scooters.

# APPLICATION

Servo LML 2T Oil is recommended for lubrication of two stroke 2 wheelers manufactured by LML Ltd. Kanpur.   The recommended dosage is 20 ml of oil per litre of petrol.

DESCRIPTION

Servo LML 2T Oil is low smoke semi-synthetic  two stroke engine oil developed to meet the critical requirements of high performance two stroke engines manufactured by M/s. LML Ltd.  It is blended from selected base stocks and additives to minimise spark plug fouling and preignition, prevent rusting, minimise deposit formation and provide protection against seizure, scuffing and wear.  It contains a diluent for easy mixing with gasoline.