# GRADES AVAILABLE – SERVO PUMP SET OIL 30, 40

# CHARACTERISTICS

| SAE GRADE | 30 | 40 |
| --- | --- | --- |
| Kinematic Viscosity @ 100(C, cSt | 10 – 12 | 13 – 15 |
| Viscosity Index, Min | 95 | 90 |
| Flash Point, COC, (C, Min | 220 | 225 |
| TBN, mg, KOH/gm | 3.8 – 5.0 | 3.8 – 5.0 |

# Text boxes

# PERFORMANCE BENEFITS

- Low maintenance cost

- Enhanced engine life

- Less wear and tear

# APPLICATION

Servo Pump set oils are recommended for slow, medium and high speed stationary diesel engines equipped on agricultural pump sets operating on HSD or LDO.

DESCRIPTION

Servo Pump set oils are blended from highly refined base stocks and a combination of anti-oxidant, anti-wear and anti-foam additives to meet the lubrication requirement of agriculture pump sets.