# GRADES AVAILABLE - SERVO HMT GEAR OIL 90

# CHARACTERISTICS

| SAE GRADE | HMT Gear |
| --- | --- |
| Kinematic Viscosity cSt @ 100(C | 16-18 |
| Viscosity Index, Min. | 90 |
| Flash point (COC), (C Min. | 180 |
| Pour Point, (C Max. | (-) 9 |

# Text boxes

# PERFORMANCE STANDARDS

Servo HMT Gear oil meets:

- API Service GL 4

- IS: 1118-1957 (Reaffirmed 1993)

- UK Defence CS 3000A

- US military MIL-L-2105

#### MANUFACTURERS APPROVAL

Approved as Genuine oil for HMT Tractors.

# PERFORMANCE BENEFITS

Servo HMT Gear oils

- Satisfy the lubrication requirements of a wide variety of gears.

- Provide protection against wear, due to good EP characteristics

- Give long service life even under high temperature operation since it has excellent oxidation stability

- Provide good protection against corrosion

DESCRIPTION

Servo HMT Gear oil is extreme pressure automotive gear lubricants.  These oils are blended from selected base stocks and contain additives to provide extreme pressure, anti-rust-corrosion characteristics

# APPLICATION

Servo HMT Gear oil is recommended as gear lubricant for HMT Tractors.  Servo HMT Gear is specially designed for power transmission units and moving equipments of Tractors.