# GRADES AVAILABLE - SERVO PRIDE GEO ALT 20W-50

# CHARACTERISTICS

| SAE GRADE | 20W-50 |
| --- | --- |
| Kinematic Viscosity cSt @ 100(C | 17.5 – 19.5 |
| Viscosity Index, Min. | 120 |
| Flash point (COC), (C Min. | 200 |
| Pour Point, (C Max. | (-) 21 |
| TBN mg KOH/gm | 5-6 |

# Text boxes

# PERFORMANCE STANDARDS

Servo Pride GEO ALT 20W-50 meets the following specifications.

- CES 20074 of Cummins USA

#### MANUFACTURERS APPROVAL

- Ashok Leyland Ltd, Chennai- Oil change every 10,000 Kms.

# PERFORMANCE BENEFITS

- Excellent resistance to oxidation and nitration.

- Excellent resistance to corrosion.

- Extra protection for valve guide seats against wear.

DESCRIPTION

Servo Pride GEO ALT 20W-50 is a high performance low ash gas engine oils, formulated from high quality mineral oil and select additive system to provide excellent thermal stability and resistance to oxidation and nitration.

# APPLICATION

Servo Pride ALT GEO 20W-50l is recommended for Ashok Leyland commercial vehicles operating   CNG.