# GRADES AVAILABLE - SERVO BRAKE FLUID DOT 4

#### CHARACTERISTICS

| GRADE | Servo Brake Fluid DOT 4 |
| --- | --- |
| Kin. Viscosity @ (-)40ºC, cSt, Max 100ºC cSt, Min | 1300 2.0 |
| Equilibrium Reflex Boiling Point, ºC, Min | 240 |
| pH Value | 8.5 – 10.5 |

# Text boxes

# PERFORMANCE STANDARDS

- SAE J 1703 for Hydraulic Brake Fluid, Heavy Duty

- FM VSS No. 116 DOT 4.

# PERFORMANCE BENEFITS

- Prevents vapour lock problems in high temperature operating conditions.

- Has improved low temperature characteristics and can be safely used in cold climate.

- Provides excellent protection against corrosion to iron, non-ferrous metals and zinc alloys.

- Ensures long service life of Brake Fluid and components of brake mechanism.

# APPLICATION

Servo Brake Fluid DOT 4  is recommended for various hydraulic brake systems including disc type operating in various new generation automobiles.

### DESCRIPTION

Servo Brake Fluid DOT 4 is a heavy duty hydraulic brake fluid processed from carefully selected ingredients and incorporates a balanced combination of anti-oxidants, metal deactivator and corrosion inhibitor.