# GRADES AVAILABLE - SERVO POWER BRAKE ALT

# CHARACTERISTICS

| Appearance | Clear Homogeneous red liquid |
| --- | --- |
| Equilibrium Reflex Boiling Point, (C Min. | 205 |
| Kinematic Viscosity, cSt @ (-) 40 (C, Max. @ 100 ( C, Min. | 1500 1.5 |
| pH Value | 7.0-11.5 |

# Text boxes

# PERFORMANCE BENEFITS

Servo Power Brake ALT

- Ensure smooth clutch operation.

- Provides excellent protection against corrosion to iron, non-ferrous metals and zinc alloys

- Has longer service life, due to excellent oxidation stability

# PERFORMANCE STANDARDS

Servo Power Brake ALT meets the following specification:

- SAE J 1703

- FMVSS 116.3

- IS:8654-1986

MANUFACTURERS APPROVAL

- Ashok Leyland Limited, Chennai

DESCRIPTION

Servo Power Brake ALT is heavy duty hydraulic brake fluid which ensures long service life of the brake fluid and components of brake mechanism. It remains clear and uniform fluid under extreme cold climatic conditions, enabling satisfactory operation of brake systems.

This formulation is successfully adopted for clutch operation of Ashok Leyland tippers.

# APPLICATION

Servo Power Brake ALT is recommended for use in clutch operation of Ashok Leyland tippers.