GRADES AVAILABLE - SERVOSYNTH SJ 5W-40

# CHARACTERISTICS

| SAE GRADE | 5W-40 |
| --- | --- |
| Kin. Viscosity @ 100ºC, cSt | 13.0 – 14.0 |
| Viscosity Index, Min | 150 |
| Flash Point, COC, ºC, Min | 200 |
| Pour Point, (C, Min. | (-) 51 |
| TBN, mg KOH/gm | 9 – 11 |

# Text boxes

# PERFORMANCE BENEFITS

- Superior wear protection.

- Superior deposit control.

- Extended component life.

- Excellent engine cleanliness.

- Lower oil consumption

- Better Fuel Economy

- Catalytic Convertor Compatible

# PERFORMANCE STANDARDS

- API SJ for Petrol and API CF in diesel service.

- Meets ACEA A3/B3 – 98, VW 502.00/505.00, MB 229.1

# APPLICATION

Servosynth SJ oil is recommended for new generation imported and Indian passenger cars using petrol and light duty diesel vehicles operating under widely varying ambient conditions.

DESCRIPTION

Servosynth SJ oil is a semi-synthetic superior performance engine oil recommended for new generation passenger cars and light duty  diesel vehicles.